## Slide 1: Rexroth Shaftless Drive Training

## Slide 2: Synopsis:
Tirupati:
Comparison between Tirupati and MMN shaftless drives.
Tirupati Drive Configuration
Motion Logic Controller
Device Status
Parking Axis
Parameter Monitoring
Oscilloscope
MMN Chennai:
Comparison between MMN A and MMN B/C press.
MMN A Configuration
Drive Specification.
Software
Parameter Backup
OFC intensity adjustment
Encoder oscilloscope Function

## Slide 3: Comparison
Tirupati
Hardware:
Single MLC is used to control all the drives in the Press.
Sercos3 communication protocol is used(Ethernet).
Dual axes inverter is used for Infeed and Drag motor.
Parking Axis is used for deactivating drives.
Software:
Indraworks
MMN Chennai
Hardware:
Each tower consists of a PPC-R which control the drives of that particular tower only.
Sercos2 communication protocol is used(OFC).
Only single axis inverter is used for all motors.
Deactivation is done through syntop.
Software:
Syntop 13 v8,Indraworks

## Slide 4: Rexroth Shaftless Drive System-Tirupati Press:
In Tirupati Press, the shaftless technology is based upon Motion Logic Controller(MLC).
The MLC acts as Master and the drives act as slaves.
The main features of this MLC system include,
  SERCOS III-master slave interface(LAN cables)
  8MB RAM
  Intel Celeron M with 1.0GHZ processor

## Slide 5: Shaftless Drive configuration Tirupati Press:

## Slide 8: Configuration:

## Slide 9: Motion Logic Controller(MLC):
L65 motion controller program can be accessed in PC through LAN network by IP address.
Program in MLC here is written using Structured text Language.
Two or three program Backups can be stored in FTP server which is available in MLC.

## Slide 10: Structured text Program:

## Slide 11: Drive basic Configuration:
The drive basically consists of three section. They are,
  Power section
  Control section
  Firmware section
Single axis and dual axes inverters are used.
Dual axes is used for infeed and drag motors.
Drag motors used here are synchronous motors.

## Slide 12: Monitoring Device status:
In Indraworks s/w, go to diagnostics menu and click device status option.
By Clicking device status option, you will be able to monitor the current status of all the devices connected to MLC.
From the status bit display, you can identify the following status of the devices,
  S-Standstill
  P-Target Position Reached
  V-In velocity
  R-Homed
  Y-Synchronized

## Slide 13: Device status:

## Slide 14: Parking Axis:
It is the method used for deactivating the drive from the control loop if it has any issues.
In MLC, an option is available to park certain axis if it has any issues. All other real axes will run fine without the axis which is parked.
To Park the device right click on the particular device  Parking axis
The desired drive can be selected from the list of drives displayed.

## Slide 15: Parking axis selection:

## Slide 16: Parameter monitoring:
Parameters of drives and motors can be viewed through Indraworks s/w for monitoring and diagnosis.
Click L65 motion controller menu
Then click parameters  Parameter Group.
The screen displays list of all the parameters and from that list you can choose the desired one.

## Slide 17: Parameter Group:

## Slide 18: Oscilloscope Function:
By using the oscilloscope function, the graphical representation for each parameter can be drawn.
To use the function go to Diagnostics Oscilloscope.
Graphs can be viewed for single device or multiple devices by clicking the Signal option.
Three types of triggering can be used for plotting the graph. They are Automatic, Manual and Signal trigger.
After selecting trigger option, the graph is plotted as shown in the figure below.

## Slide 19: Oscilloscope Model Graph:
Inference: For diagnosis and predictive Maintenance

## Slide 20: Comparison
MMN A press:
Indradrive(Common DC bus)
Syntop 13 V8
No guide motor drives.
Firmware V13 is used in PPC-R
LED display with operation controls.
Folder RTF motor drive changed to balloon shaftless cabinet.
MMN B/C press:
DKR drive (No common DC bus)
Syntop 6 v15
Guide motor drives deactivated.
Firmware V8 is used in PPC-R.
Only Error code display.

## Slide 21: MMN Shaftless system:
PPC-R Primary Link

## Slide 22: Drive Inner Loop:

## Slide 27: Supply Units:

## Slide 28: Type Plate:

## Slide 31: Drive basic Configuration:
The drive basically consists of three sections. They are,
  Power section
  Control section
  Firmware section
Features of new MMN drives,
  SERCOS II(optic fibre)
  LCD display with controls.
  Common DC bus

## Slide 32: Power Section Types:

## Slide 34: HMS01 Drive:
Drives are mainly used for achieving speed and phase synchronization.

## Slide 35: Type Code:

## Slide 36: HMS power section:

## Slide 37: Control Section:

## Slide 42: Softwares Used:
Software used are as follows,
  Syntop 13 V8
  Indra works
Parameters can be viewed and downloaded using syntop 13 s/w.
Oscilloscope function is done using Indra works s/w.

## Slide 43: Parameter Backup:
Open and configure SCP configurator for respective PPC-R.
Once configured, directly connect to Motion Control. Thus, online connection is established.
Then use the option Load/save parameter to upload/download the parameters from PPC-R.
You can download S/P parameters individually.

## Slide 44: SCP configurator:

## Slide 45: Optic Fibre Intensity adjustment:
1. press and hold both esc and enter key for 8 seconds
2.Press up arrow. command screen will appear
3. Press Enter
4.Press Up arrow. 2.2 screen will appear
5.Press Enter. P4027 will appear. Press enter
6. default setting will be 15..30m
7. Press up or down button to increase or decrease
8. Highest value is >45m. So once the range is selected press enter.
9.Press esc to main screen
SERCOS Primary/Secondary LOOP adjustment
Inner Loop adjustment in LED display(Drive to Drive)

## Slide 46: Encoder oscilloscope function:
By using the oscilloscope function, the graphical representation for each parameter can be drawn.
Open Indraworks s/w
Select Diagnosis/service---->oscilloscope function in the appeared screen.
Add parameters from the list of S and P Parameters.
Triggering signal can be manual or Signal form.
Uses of Oscilloscope function,
  Encoder Signal strength check
  Graphical representation for diagnosis

## Slide 47: Oscilloscope Function:

## Slide 48: Sample Graph:

## Slide 49: Encoder Signal Strength:
X coordinate-Sine signal
Y coordinate-Cosine signal
Shape
  Round-Good
  Elliptical-Bad

## Slide 50: Encoder Lissajous wave form decision criteria:

## Slide 51: Question and Answer threads
B link register only modified, W word register not modified.
Idea to replace broken thermistor was discussed.
Gain adjustment and homing adjustment for drives was discussed.
Fibre optic measurement should be taken at 650nm wavelength. Range is –20dB for Primary, secondary and inner loop also.
PLC modified Program list with backup was given.

## Slide 52: Thank you